PRE-FLIGHT INSPECTION

COCKPIT PREPERATIONS

| 1 | All chocks,tiedowns and pitot cover removed | CHECK |
| --- | --- | --- |
| 2 | Parking brake / Brakes | CHECK FREE MOVEMENT, PRESSURE & FLUID LEVEL – SET ON |
| 3 | Fire extinguisher & First aid kit | CHECK |
| 4 | Aircraft documents | CHECK |
| 5 | Magneto switches | OFF – KEY OUT |
| 6 | Avionics master switch | OFF |
| 7 | Fuel shutoff valve | ON |
| 8 | Main fuses | PUSH IN |
| 9 | Master switch | ON |
| 10 | Anti – collision lights & Landing lights | CHECK & OFF |
| 11 | Electric fuel pump | CHECK & OFF |
| 12 | Master switch | OFF |
| 13 | Seatbelts & shoulder harnesses | CHECK CONDITION & SECURITY |
| 14 | Aileron cable mounting & rod ends | CHECK FOR FREE ROTATION & EXCESSIVE MOVEMENT, BOLTS & ANCHORS ON REAR OF SEATS SECURE. |
| 15 | Elevator cable mounting & rod end | CHECK FOR FREE ROTATION & EXCESSIVE MOVEMENT, BOLT & ANCHOR ON MAIN BEAM SECURE. |
| 16 | Throttle | CHECK MOVEMENT & MOUNTING. |
| 17 | Rudder & nose wheel steering pushrods & ends | CHECK SECURITY & FREE MOVEMENT. |
| 18 | Flaps | SET FIRST STAGE. CHECK FOR FREE MOVEMENT, EXCESSIVE PLAY & BOLT SECURE. CHECK ROD ENDS / CONTROL LINKAGE FOR EASE OF ROTATION. |
| 19 | Trimmer | EXCERSISE – SET NEUTRAL |
| 20 | Fuel Contents | CHECK |

### 1

### EXTERNAL CHECKS

| 1 | Port undercarriage | CHECK MAIN LEG SECURITY & BOLTS, SPEED FAIRING SECURITY, WHEELS & BRAKES, HYDRAULIC LINES, TYRE INFLATION, CREEP MARKS AND CONDITION. |
| --- | --- | --- |
| 2 | Port wing strut | CHECK LOWER AND UPPER ATTACHMENTS (BOLTS MUST NOT BE TIGHT) GENERAL CONDITION OF STRUT. SECURITY OF UPPER SPEED FAIRING. |
| 3 | Port wing – Root mount bolts | CHECK BOLT SECURITY. CHECK LOWER COVER FAIRING & TOP COVER STRIP SECURITY. |
| 4 | Port wing – Flap | CHECK SECURITY. CHECK HINGE SECURITY & LUBRICATION. CHECK ROD ENDS FOR EASE OF ROTATION/EXCESSIVE MOVEMENT & BOLT SECURITY. |
| 5 | Port wing – Trailing Edge | CHECK AILERON FREEDOM OF MOVEMENT/SECURITY. HINGES LUBRICATED, PINS SECURE. CHECK AILERON CABLE ROD END FOR EASE OF ROTATION/EXCESSIVE MOVEMENT/BOLT SECURE. |
| 6 | Port wing – Tip | CHECK FOR DAMAGE, LIFT TIP TO CHECK STRUT/WING SECURITY & ROCK FORE – AFT TO CHECK UNDERCARRIAGE LEG SECURITY. |
| 7 | Port wing – Aileron attachment | CHECK THROUGH INSPECTION WINDOW FOR CABLE SECURITY. |
| 8 | Port Wing – Leading edge | CHECK STALL WARNING APATURE CLEAR OF OBSTRUCTIONS AND TEST OPERATION BY CAREFUL SUCTION. CHECK LEADING EDGE FOR DAMAGE. |
| 9 | Port door & window | SECURE & UNDAMAGED. LATCHES & HINGES SECURE AND OPERATIONAL. |
| 10 | Windscreen | CLEAN & UNDAMAGED |
| 11 | Port Nose | VENTS CLEAR. LOWER COWL SECURE. |
| 12 | Nose Leg | CHECK SECURITY. CHECK WHEEL SECURITY/AXLE NUT. TYRE INFLATION, CONDITION & CREEP MARKS. SUSPENSION RUBBERS. |
| 13 | Propeller & Spinner | CHECK CONDITION & SECURITY |
| 14 | Remove Top Cowl (Daily inspection) | CHECK SECURITY OF ENGINE MOUNTS, ENGINE COMPONENTS & SYSTEMS, SPARK PLUGS, WIRING, FUEL LINES, BAFFLES ETC. LOOK FOR OIL LEAKS. CHECK OIL LEVEL/TOP UP IF NECESSERY. CHECK BATTERY FLUID LEVEL. CHECK OIL OVERFLOW BOTTLE LEVEL. |
| 15 | Replace Top Cowl | ENSURE FRONT LUGS ARE ENGAGED AND MAIN CLIPS SEATED AND PINNED CORRECTLY. CHECK FOR ALIGNMENT OF RAM AIR DUCTS AND SEALS. |
| 16 | Starboard nose | VENTS CLEAR. LOWER COWL SECURE. |
| 17 | Starboard door & window | SECURE & UNDAMAGED. LATCHES & HINGES SECURE AND OPERATIONAL. |
| 18 | Starboard undercarriage | CHECK MAIN LEG SECURITY & BOLTS, SPEED FAIRING SECURITY, WHEELS & BRAKES, HYDRAULIC LINES, TYRE INFLATION, CREEP MARKS AND CONDITION. |

2

| 19 | Starboard wing strut | CHECK LOWER AND UPPER ATTACHMENTS (BOLTS MUST NOT BE TIGHT) GENERAL CONDITION OF STRUT. SECURITY OF UPPER SPEED FAIRING. |
| --- | --- | --- |
| 20 | Starboard wing – Root mount bolts | CHECK BOLT SECURITY. CHECK LOWER COVER FAIRING & TOP COVER STRIP SECURITY. |
| 21 | Starboard wing – Leading edge | CHECK LEADING EDGE FOR DAMAGE. |
| 22 | Starboard wing – Tip | CHECK FOR DAMAGE, LIFT TIP TO CHECK STRUT/WING SECURITY & ROCK FORE – AFT TO CHECK UNDERCARRIAGE LEG SECURITY. |
| 23 | Starboard wing – Aileron attachment | CHECK THROUGH INSPECTION WINDOW FOR CABLE SECURITY. |
| 24 | Starboard wing – Trailing Edge | CHECK AILERON FREEDOM OF MOVEMENT/SECURITY. HINGES LUBRICATED, PINS SECURE. CHECK AILERON CABLE ROD END FOR EASE OF ROTATION/EXCESSIVE MOVEMENT/BOLT SECURE. |
| 25 | Starboard wing - Flap | CHECK SECURITY. CHECK HINGE SECURITY & LUBRICATION. CHECK ROD ENDS FOR EASE OF ROTATION/EXCESSIVE MOVEMENT & BOLT SECURITY. |
| 26 | Transponder antenna | CONDITION & SECURITY |
| 27 | Fuel drain | SAMPLE CHECK FOR WATER/CONTAMINANTS. |
| 28 | Fuselage drain holes | CHECK CLEAR |
| 29 | Rear window | UNDAMAGED & CLEAN |
| 30 | Starboard side ventral fin | SECURE. CHECK DRAIN HOLE & TIE DOWN EYE SECURITY. |
| 31 | Starboard tailplane | CONDITION & SECURITY |
| 32 | Tail fin | CONDITION & SECURITY |
| 33 | Static source | CHECK CLEAR |
| 34 | Elevator | CONDITION/HINGES SECURE AND LUBRICATED. HINGE PINS SECURE. TRIM TABS SECURE. FULL & FREE MOVEMENT. |
| 35 | Rudder | CONDITION/HINGES SECURE & LUBRICATED. HINGE PINS SECURE. FULL & FREE MOVEMENT (WITH NOSEWHEEL OFF THE GROUND) CHECK CABLE ROD END FOR EASE OF ROTATION/EXCESSIVE MOVEMENT. BOLT SECURE. |
| 36 | Strobe lamps | CONDITION & SECURITY |
| 37 | Port tailplane | CONDITION & SECURITY |
| 38 | Port side ventral fin | CONDITION & SECURITY |
| 39 | Fuel filler cap | SECURITY |
| 40 | Port side rear window | UNDAMAGED & CLEAN |
| 41 | Flaps | UP |

3

#### INTERNAL CHECKS

| 1 | External checks | COMPLETE |
| --- | --- | --- |
| 2 | Flaps | UP |
| 3 | Doors | CLOSED & SECURE |
| 4 | Harnesses | ADJUSTED & SECURED |
| 5 | Baggage | SECURE |
| 6 | Brakes | PARK POSITION |
| 7 | Fuel shut off valve | CHECK ON |
| 8 | Flying controls | FULL & FREE MOVEMENT |
| 9 | Instruments & Gauges | CHECK |
| 10 | Trim | EXERSIZE – SET TAKE OFF |
| 11 | Throttle | EXERSIZE – SET CLOSED |
| 12 | Carb heat | EXERSIZE – SET COLD |
| 13 | Magnetos | CHECK – OFF |
| 14 | Avionics Master | CHECK – OFF |

STARTING ENGINE

| 1 | Master Fuses | PUSH IN |
| --- | --- | --- |
| 2 | Circuit Breakers | CHECK - ON |
| 3 | Master Switch | ON |
| 4 | Strobes | ON |
| 5 | MAGNETO’S | CHECK OFF |
| 6 | Fuel Pump | ON |
| 7 | Choke | FULL ON |
| 8 | Pull Prop though 6 times | PRIME ENGINE FUEL |
| 9 | Fuel Pump | OFF |
| 10 | Throttle | CHECK - CLOSED |
| 11 | LOOKOUT | GOOD LOOK AROUND. SHOUT ‘CLEAR PROP’ |
| 12 | Magnetos | KEY IN – OPERATE STARTER |
| 13 | Throttle | SET IDLE 1000 –1200 RPM |
| 14 | Oil Pressure | CHECK RISING (SHUT DOWN IF NO RISE IN 10 SEC) |
| 15 | Starter Motor Warning Light | CHECK OUT |
| 16 | Choke | CLOSE GRADUALLY. MAINTAIN ENGINE IDLE SPEED |
| 17 | Warm – up engine | 1200RPM UNTIL 50 DEG C. |
| 18 | Instrument T’s & P’s | CHECK ALL |
| 19 | Avionics | MASTER ON – RADIO ETC ON. |

4

TAXI-ING CHECKS

| 1 | Radio | CHECK READABILITY |
| --- | --- | --- |
| 2 | Obtain Taxi clearance | ATC |
| 3 | Altimeter | SET |
| 4 | Brakes | CHECK |
| 5 | Rudder / Nosewheel | CHECK FULL MOVEMENT |
| 6 | Turn & Slip / Compass / DI | CHECK IN TURNS |

POWER CHECKS

| 1 | Temperature | CHECK 50 DEG C. |
| --- | --- | --- |
| 2 | Fuel | CHECK ON / CONTENTS |
| 3 | Temperatures & Pressures | CHECK |
| 4 | Check clear behind | SET 2000rpm HOLD 10 sec. |
| 5 | Check Magnetos | DROP NOT TO EXCEED 100rpm |
| 6 | Carb Heat | CHECK RPM DROP / TEMP INCREASE. |
| 7 | Alternator Load | WITHIN LIMITS |
| 8 | Slow Running | CHECK IDLE |
| 9 | Set throttle | 900-1200rpm |
| 10 | Carb heat | APPLY FOR 30 sec. |

PRE TAKE-OFF CHECKS

| 1 | Flaps | SET 1ST STAGE |
| --- | --- | --- |
| 2 | Trimmer | SET TAKE-OFF |
| 3 | Fuel | PUMP ON |
| 4 | Carb Heat | CHECK – OFF |
| 5 | DI / Compass | ALIGHNED |
| 6 | Magnetos | BOTH ON |
| 7 | Gyros & Instruments | CHECK |
| 8 | Doors / Harnesses | CHECK LOCKED |
| 9 | Flight Controls | FULL & FREE |
| 10 | Cylinder Head Temperatures | CHECK 100 DEG C. BEFORE OPERATING FULL THROTTLE |

5

TAKE OFF

| 1 | Flaps | 1ST STAGE |
| --- | --- | --- |
| 2 | Carb Heat | CHECK – OFF |
| 3 | Throttle | FULL OPEN |
| 4 | Elevator Control | LIFT NOSE WHEEL AT 40-45 KIAS WAIT FOR AIRCRAFT TO FLY ITSELF OFF AT APPROX. 55 KIAS |
| 5 | Climb Speed / Flaps | 65 KIAS UNTIL FLAPS RETACTED AT 300FT. THEN CLIMB AT 72 KIAS. |
| 6 | CHT’S | CHECK (100 – 200 DEG C.) |
| 7 | Fuel Pump | OFF AT TOP OF CLIMB |
| 8 | Brakes | APPLY THEN OFF TO STOP WHEELS SPINNING. |

ENROUTE CHECKS (IFREDAC)

| I | Icing | NONE PRESENT ON AIRFRAME. CARB HEAT - ON. |
| --- | --- | --- |
| F | Fuel | CONTENTS SUFFICIENT |
| R | Radio | CORRECT FREQUENCY SET |
| E | Engine | CHT’s, OIL PRES. TEMP. ETC. |
| D | D/I | ALIGHN WITH COMPASS |
| A | Altimeter | CORRECT SETTING |
| C | Carb Heat | CARB HEAT – OFF. |

DOWNWIND CHECKS (CABFLICH)

| C | Carb Heat | ON |
| --- | --- | --- |
| A | Altimeter | SET AIRFIELD QFE |
| B | Brakes | CHECK – OFF |
| F | Fuel | PUMP ON |
| L | Landing lights | ON |
| I | Instruments | T’s & P’s. D/I & COMPASS |
| C | Carb Heat | AS REQUIRED. OFF ON SHORT FINAL. |
| H | Harnesses & Hatches | SECURE |

6

LANDING

| 1 | Reduce speed | 70 KIAS MAX |
| --- | --- | --- |
| 2 | Flaps | FULL FLAPS |
| 3 | Carb Heat | OFF (SHORT FINAL) |
| 4 | Approach Speed | 55 – 57 KIAS |

AFTER LANDING

| 1 | Flaps | UP |
| --- | --- | --- |
| 2 | Fuel Pump | OFF |
| 3 | Carb Heat | OFF |

SHUTTING DOWN

| 1 | Brakes | SET PARK |
| --- | --- | --- |
| 2 | Magnetos | CHECK BOTH |
| 3 | Radio / Transponder / GPS | OFF |
| 4 | Landing Lights | OFF |
| 5 | Magnetos | OFF |
| 6 | Key | OUT |
| 7 | Strobes | OFF |
| 8 | Avionics Master | OFF |
| 9 | Master | OFF |
| 10 | Main Fuses | PULL OUT |
| 11 | Control Locks | IF REQUIRED |
| 12 | Tie downs & Cover | IF REQUIRED |

| STALL CLEAN | 47 KIAS |
| --- | --- |
| STALL FULL FLAPS | 43 KIAS |
| BEST GLIDE | 72 KIAS |
| ENGINE FALIURE AFTER TAKE OFF | 60-65 KIAS |
| APPROACH SPEED NORMAL (WITH FULL FLAPS) | 57 KIAS |
| APPROACH SPEED – SHORT FIELD | 55 KIAS |
| APPROACH SPEED (CLEAN) | 70 KIAS |
| BEST MANOUVERING | 91 KIAS |

V – SPEEDS

7

G-**** :	 JABIRU 450 SPL

SERIAL NUMBER: PFA ****-****

CHECKLIST

| EMPTY WEIGHT kgs | PILOT kgs | PASSENGER | SUB TOTAL kgs | FUEL ltrs | FUEL WEIGHT kgs | TOTAL kgs |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | St. | Kgs |  |  |  |  |
| 268.00 | 81.00 | 11 | 70.0 | 419.0 | 43 | 31.0 | 450 |
| 268.00 | 81.00 | 12 | 76.4 | 425.4 | 34 | 25.0 | 450 |
| 268.00 | 81.00 | 13 | 82.8 | 431.8 | 25 | 18.0 | 450 |
| 268.00 | 81.00 | 14 | 89.1 | 438.1 | 17 | 12.0 | 450 |
| 268.00 | 81.00 | 15 | 95.5 | 444.5 | 8 | 6.0 | 450 |
| 268.00 | 81.00 | 16 | 101.8 | 450.8 | 0 | 0 | 450 |
| 268.00 | 81.00 | 16 | 101.8 | 450.8 | 15 | 10.8 | 461 |
| 268.00 | 81.00 | 17 | 108.1 | 457.1 | 15 | 10.8 | 468 |
| 268.00 | 81.00 | 18 | 114.5 | 463.5 | 15 | 10.8 | 475 |
| 268.00 | 81.00 | 19 | 121.0 | 470.0 | 15 | 10.8 | 481 |
| 268.00 | 81.00 | 20 | 127.0 | 476.0 | 15 | 10.8 | 489 |