Jabiru J400   G-REAF    Checklist	  V2 14/9/2010

Documents complete

Remove tie-downs, remove pitot & static covers - check no blockages

Check fuel drains, check fuel quantity, check fuel filler caps secure

Remove cowling, check all secure, no oil leaks, check oil level

Walk-round	Windscreen - clean if necessary

Wheels secure, tyres inflation, brakes no leaks

Control surfaces - check secure, check free movement, check 			  	rod ends free

Propellor - check for damage, check spinner secure

Stall-warner - check

Engine		Fuel on

pull-through	Throttle closed, choke on, fuel pump on, master switch on

Pull through 6 blades

Fuel Pump off, master switch off

Internally		Aileron cables 	- check security

Elevator cables 	- check security

Rudder push-rods 	- check

Brakes 		- check lever travel & pressure, set on

Flap lever 		- check secure & free travel

Throttle & carb heat - check full & free travel

Seat belts on

Loose items 		- secure

Check fuel

Starting		Carb heat		- cold

Throttle		- closed

Choke		- on		(if cold, if hot no choke)

Fuel pump		- on 10 seconds, then off

“CLEAR PROP”

Master switch	- on

Ignition switch	- on

Operate starter

set idle 900-1000 rpm

Check warning lights off

check engine indications (oil pressure within 10 seconds?)

choke			- off

Warm up		Set 1200 rpm

Avionics on

Elec carb heat 	- on 1

GPS on, set radio frequencies, set transponder on, ANR on

Check contact breakers

Radio call

Set altimeter

Power checks	Min oil temp 50C

Brakes 		- on

Throttle		- set 2000 rpm

Run for 10 seconds - check engine indications

Magnetos 		- check in turn  -  max rpm drop 100

Carb heat 		- apply 10 secs - check rpm drop - carb heat off

Throttle		- set to idle  -  reset to 1200 rpm

Take-off		Doors			- secure

Seat belts		- secure

Flight controls  	- full and free movement

Elevator trim  	- neutral

Flaps			- First stage

Fuel pump		- On

Carb Heat cold

Engine temps & pressures check (min CHT 100C)

Line up

Full power

Lift nosewheel at 45 KT

Climb initially at 75 KT

Flaps off		- at min 300 ft agl

Climb at 85KT  	- check engine temperatures and pressures

Top of climb   	- fuel pump off

Cruise		Fuel, Radio, Engine T’s & P’s & carb ice check, Altimeter

Pre-landing		Seatbelts secure

Carb heat on & elec carb heat 2, 30secs before reducing power

Fuel pump on

Landing light on

Flaps 1st stage (max 80 Kt)

Landing		Flaps 2nd stage (max 70 Kt)

65 Kt

Trim

Carb Heat off at 300 ft

Lower nosewheel gently

Minimum braking

Post landing		Brake on

Flaps up

Fuel pump off

Elec equipment off & ANR off

Ignition off

Master switch off

Fuel off

Secure control column

Tie-downs & chocks

Pitot & static covers on

Aircraft cover on