| SPEEDS | NEVER EXCEED Vne MAX CRUISE Vno MANOEVERING Va FLAPS Vfe 1st Stage FLAPS 2nd Stage TURBULENT AIR CROSSWIND MAX STALL Vs1 clean Vso full flap BEST GLIDE TAKE-OFF safety speed CLIMB initial 1st stage flap short field “ normal Vx best rate of Vy best angle of APPROACH full flap short field GO ROUND accelerate to retract flaps to 1st stage accelerate to retracting flaps slowly | kts 138 124 124 80 70 91 14 51 45 65 64 75 71 85 85 85 65 65 70 85 |  | WEIGHTS BALANCE FUEL T’s & P’s | EMPTY MAX REAR SEATS max CG LIMITS 8cm - 28cm aft of datum LEVER ARMS Empty weight 353kg Pilot + front passenger Fuel header tank 4kg Fuel Rear footwell Rear seats Rear baggage shelf Ballast 1kg TOTAL USABLE OIL TEMP limits normal OIL PRESSURE min 80kpa 11psi flight min 220kpa 31psi max 525kpa 76psi FUEL PRESSURE min CHT max (5 Min) max continuous take-off min EGT max normal | kgs 353 700 120 9.84cm -1.20cm -1.20cm 45.10cm 64.00cm 103.40cm 157.00cm 408.00cm 134L 124L 50C-118C 80C-100C 0.75bar 2.0bar 5.0bar 0.15bar 175C 150C 100C 720C 640-680C |
| --- | --- | --- | --- | --- | --- | --- |
| RPM | MAX MAX CONTINUOUS FULL THROTTLE STATIC CRUISE | 3300 3150 2800-3000 2750-2850 |  | OIL TYRE PRESSURES | AERO W MULTIGRADE 15W-50 NOSEWHEEL MAINS | 3.5L 12-15psi 24psi |